Lazare CARNOT -ARRAS-		Compte rendu / Activité: Mesure d'une Masse	Act – 2 x 3h / STI2D – 2023/2024

NOM: / Prénom:			CLASSE : TDD / 10/12/2022 20:01:22

Condition:	Labo SIN, Salle 206
Matériel:	un ordinateur sous Windows avec les logiciels Proteus 8 et Flowcode 9 / TerminalRS232, XLoader / une carte de développement ( PIC , Arduino ) / un capteur de force 5 kg ou 10 kg / un module HX711
Documents:	le sujet de cette Activité

I – Capteur de force (Load cell)
une image
constitution

II – Simulation du capteur de force

Masse	0 g					5 kg
%	0%	10	20	30	40	50	60	70	80	90	100%
V	0					5 mV

Pour un capteur de force gamme 5 kg, alimenté sous 5 V.
Que peut-on en conclure ?

III – Mesure de la masse
Analyse de la documentation constructeur du HX711
Traduire les phrases suivantes
- 24-Bit Analog-to-Digital Converter (ADC) for Weigh Scales
- Two selectable differential input channels
- ... with selectable gain of 32, 64 and 128
- On-chip power supply regulator for load-cell
- Operation supply voltage range: 2.6 ~ 5.5V
- Current consumption including on-chip analog power supply regulator: normal operation < 1.5mA, power down < 1uA

Puis compléter le tableau de description des broches ci-dessous
N° de broche	Nom	Fonction	Description
1	VSUP
2
3	AVDD
4
5	AVDD
6
7	INA-
8	INA+
9
10
11	PD_SCK
12	DOUT
13
14
15
16	DVDD

Reset and Power-Down
When chip is powered up, on-chip power on rest circuitry will reset the chip. Pin PD_SCK input is used to power down the HX711.
When PD_SCK Input is low, chip is in normal working mode.
When PD_SCK pin changes from low to high and stays at high for longer than 60µs, HX711 enters power down mode (Fig.3).
When internal regulator is used for HX711 and the external transducer, both HX711 and the transducer will be powered down.
When PD_SCK returns to low, chip will reset and enter normal operation mode. After a reset or power-down event, input selection is default to Channel A with a gain of 128.

Traduction

Valeurs attendues
%	0%	10	20	30	40	50	60	70	80	90	100%
Masse	0 g	500 g				2,5 kg					5 kg
V (mV)	0	0,5				2,25					5
(Mesure)10	0	209 715				1 048 575					2 097 151
(Mesure)16	0	0x33333	0x	0x	0x	0xFFFFF	0x	0x	0x	0x	0x1FFFFF

Valeurs estimées (Simulation)
%	0%	10	20	30	40	50	60	70	80	90	100%
Masse	0	500 g				2,5 kg					5 kg
V (mV)	0	0,43									4,3
(Mesure)16	0	0x02C046	0x	0x	0x	0x	0x	0x	0x	0x	0x1B82C2
(Mesure)10	0	180 294									1 802 946

Valeurs mesurées
Masse	0	100 g	200 g	300 g	400 g	500 g	1 kg	1,5 kg	2 kg	2,5 kg	3 kg
(Mesure)10	0

Justifier les écarts, et proposer un moyen de corriger les erreurs.

Et pour les valeurs négatives ?
Valeurs (Simulation)
%	0%	-10	-20	-30	-40	-50	-60	-70	-80	-90	-100%
V (mV)	0	-0,43				-2,15					-4,3
(Mesure)16	0	0xFD3FB9	0x	0x	0x	0x	0x	0x	0x	0x	0x
C à 1		0x02C046
C à 2		0x02C047
décimal		180295
simulation	0	-180295				-901471					-1 802 942